## Slide 1
Issue | Error details | Symptom | Diagnostics | Workaround/fix
Processor configuration errors | uncorrectable errors (MLC, IFU, UPI) | OS System hangs, CPU hangs | Raw data from BMC, CPU crash dump data | Microcode 65/2C and now 69/2F in BIOS v 3.3 (X11 DP) fixes all issues
Rank switching mitigation errors | Multi-rank DIMMS errors | Flooding of correctable errors during rank switching with the following by Uncorrectable, system hangs | Not available | No yet fixed
Memory controller Failures | Known by Intel memory failures | False memory controller failures by uncorrectable errors, system hangs. There are random system reboots from time to time for no reason. | Get the CPU crash dump data to see MC 7 and MC 8 and MC12-M18 | Fix in Microcode 69/2F (to be released 3/2020, PPR workaround in latest RC code. ADC/ADDDC not fixed, VLS functions not fixed yet.
Integrated memory controller errors | memory scrubbing (uncorrectable errors) | Uncorrectable errors causes CPU hang, false-positive DIMM, system hangs, memory mapped out or memory loss | CPU crash dump data, MC12-MC18 MSR registers | RC code (open source) from Intel to Keep the scrubbing corrected Fixed in 3.3 BIOS (to be released 3/2020
Summary of the Intel Integrated Memory Controller Open Issues